## Slide 1: Covex, LLC
GMP Training: Including applicable GLPs and GCPs

## Slide 2: Purpose
This training is an overview of Good Manufacturing Practices regulation, specifically 21 CFR Part 211. The following will be addressed
  An overview of the different sections of the 21 CFR Part 210 and 211.
  Current interpretation of the regulation – “What they mean”
  How Consultants provides services to industries
  Overview of how GCP and GLP relate to GMPs
  How 21 CFR Part 11 regulations relate to GxPs

## Slide 3: 21 CFR Part 210
This section only has 3 parts (one of which is definitions)
Provides the current state of good manufacturing regulations and states non-compliance with the regulations means the drug is adulterated per the Food, Drug and Cosmetic Act.
States to which persons, groups and companies 21 CFR 211 applies (pharmaceutical companies)

## Slide 4: 21 CFR 211 Part A General Provisions 211.1-211.3
211.1 provides the scope of the regulations and states it applies to those companies that manufacture drugs as defined in the Food, Drug and Cosmetic Act.
This regulation was first issued in 1978
211.1 – Not used
211.3 Definitions: See 210.3 for applicable definitions.

## Slide 5: 21 CFR 211 Part B Organization and Personnel 211.22-211.34
211.22 – Explicitly states there must be a quality control unit. That unit is responsible for approving or rejecting all tests and products. All procedures for the unit must written and approved.
211.25 - Employees involved in the manufacturing process must have the education and training to complete their job responsibilities. This must be documented
211.28 - Employees involved in the manufacturing process must wear clean clothes, have good hygiene and follow written procedures
211.34 - Consultants must meet the same criteria set forth in 211.25 and 211.28

## Slide 6: 21 CFR 211 Part B O Organization and Personnel Application to Consultants
We must follow all procedures that are written to meet the sections regarding training and responsibilities since we are contractors.
From a system standpoint, validation may occur of the system that contains the written SOPs, the Learning management system or the employee HR system that contains job qualifications. Some Consultants may be in a QA role and have to abide by the rules outlined in 211.22

## Slide 7: 21 CFR 211 Part B Related Computerized Systems
Training systems:
  Keeps track of employee training to meet requirements set forth in 21 CFR 211.25.
  Electronically tracks versions of SOPs
  Allows groups of persons to be created to assign training to entire groups/departments
  Common software used: Eduneering and Compliance Wire
HR systems (usually not validated)
  Keeps track of CVs and resumes

## Slide 8: 21 CFR 211 Part C Buildings and Facilities 211.42-211.58
211.42 (a)– Buildings for manufacture, storage packaging, bottling and shipping have to be an adequate size and be able to be cleaned.
211.42 (b)– Buildings must be big enough for equipment to be placed to prevent mix-ups of product or contamination of product.
211.42 (c)– Operations must prevent contamination and mix-ups. There are listed items that are specifically addressed including cleaning the area, equipment, environmental monitoring and maintaining aseptic conditions
211.44- There must be adequate lighting.

## Slide 9: 21 CFR 211 Part C Buildings and Facilities 211.42-211.58 – Cont
211.46 – Adequate ventilation with positive pressure. It should control air pressure, micro-organisms, dust, humidity, and temperature. Air filters must be used and changed regularly.
211.48 – Plumbing Potable water shall be supplied under continuous positive pressure will not contaminate drug product. Must meet EPA standards. Water not meeting such standards shall not be permitted in the potable water system.
(b) Drains shall be of adequate size and, where connected directly to a sewer, shall be provided with an air break or other mechanical device to prevent back-siphonage.

## Slide 10: 21 CFR 211 Part C Buildings and Facilities 211.42-211.58 – Cont
211.50 -Sewage, trash, and other refuse in and from the building and immediate premises shall be disposed of in a safe and sanitary manner.
211.52 - Adequate washing facilities including hot and cold water, soap or detergent, air driers or single-service towels, and clean toilet facilities easily accessible to working areas.
211.56 – Sanitation: buildings must be clean, free of rodents, birds, insects and other vermin. Written procedures are required to prevent contamination of equipment from insecticides, pesticides etc.
211.58 – Maintenance: Any building used in the manufacture, processing, packing, or holding of a drug product shall be maintained in a good state of repair.

## Slide 11: 21 CFR 211 Part C Buildings and Facilities Application to Consultants
Consultants may provide services to validate individual systems within the facility. These include, HVAC (positive air flow), temperature and humidity monitoring (211.46), and building management systems. Overall validation of a new building is also possible, but that is usually broken down into individual systems.
Consultants can also provide documentation of cleaning validation (211.42).

## Slide 12: 21 CFR 211 Part C Related Computerized Systems
Building Management systems
  Used to keep track of specific “points” in a buildings mechanical and electrical equipment such as ventilation, lighting, power systems, fire systems, and security systems
  Common software: Johnson Controls and Siemens
Temperature and Humidity Monitoring
  Related to the HVAC system, this system independently monitor the temperature and humidity in an area and sends alarms when out of specification readings are obtained.
  Common software: Dickson and Sesni-Tech/Sensi-Guard

## Slide 13: 21 CFR 211Part D Equipment 211.63-211.72
211.63 – Equipment needs to be the right design, size, and located in a place that makes sense for its purpose. It must be able to be cleaned and maintained.
211.65 – The parts of equipment that comes in contact with the product cannot contaminate the product. Also, lubricants, coolants and other substances in the equipment should not contaminate the product.
211.67 – Equipment and utensils must be kept clean and maintained. Written procedures are required. See regulations for specific items required in the written procedure.

## Slide 14: 21 CFR 211 Part D Equipment 211.63-211.72-Cont
211.68 – Automatic, mechanical and electronic equipment can be used for production. It needs to have routine calibration and maintenance. Systems have to be controlled (limited to authorized users), validated and any inputs and outputs need to be validated. Data from these systems need to be backed up.
211-72: Filters for liquids can’t release fibers into liquids. If you have to use a filter that will release fibers, a second filter is required. No asbestos filters.

## Slide 15: 21 CFR 211 Part D Equipment Application to Consultants
Documentation and validation of the different pieces of equipment used to manufacture the product. Especially those that fall under 211.68, which include computerized systems.
Documentation and validation of Calibration and Preventative Maintenance tracking systems that are mentioned in 211.68

## Slide 16: 21 CFR 211 Part D Equipment Related Computerized Systems
Individual equipment control software
  The actual software or PLC that controls the equipment.
Manufacturing Control systems
  Systems that controls several or all the pieces of equipment at once.
  Common software used: Delta V and Honeywell Experian
PM and Calibration Tracking systems
  System that list each piece of equipment, when the PM or calibration is due and if it was completed.
  Common software used: Blue Mountain

## Slide 17: 21 CFR 211 Part E Control of Components and Drug Product Containers and Closures 211.80-211.94
211.80- Written procedures for receipt, ID, handling, testing and approving of product. Components must be stored properly. Bags and Boxes can’t be kept on the floor. Distinctive codes (Lot numbers) need to appear on containers/ groups of containers. The code will be used to identify the disposition of the lot.
211.82 – Products must be inspected after receipt and before acceptance. Items must be segregated from accepted product until testing and acceptance is complete.

## Slide 18: 21 CFR 211 Part E Control of Components … 211.80-211.94, Continued
211.84 – For each lot, a representative sample needs to be taken, tested and either approved or rejected. While the testing occurs the lot in question needs to be segregated from “in use” material. Identity conformity, purity, strength, and quality should be tested.
211.86 – Oldest stock should be used first.
211.87 - Stock should be retested after time or if exposed to air, heat or other conditions that can affect it

## Slide 19: 21 CFR 211 Part E Control of Components … 211.80-211.94, Continued
211.89 – Rejected components need to be identified and quarantined so they are not used in production.
211.94 – Containers and closures should not alter the safety, identity, strength, quality, or purity of the drug beyond specified amounts. The containers should protect against outside conditions and they should be clean and sterilized if necessary. There needs to be written procedures for the testing, cleaning and sterilization of containers.

## Slide 20: 21 CFR 211 Part E Equipment Application to Consultants and Related Computerized Systems
Consultants could be involved with the instrumentation that tests the containers and the product in the container.
The systems that test these are specific to the product being tested. In general, consultants could see FTIRs testing for identity and purity of product. However, any other laboratory equipment could be used.

## Slide 21: 21 CFR 211 Part F Production and Process Controls 211.100-211.115
211.100 – Written procedures for the production to ensure the identity, strength, quality, and purity of the product. Creation of the product must documented (batch record) and any deviation from the process must be documented and justified.
211.101 – The creation of the product must be done to obtain 100% of the labeled amount of the active ingredient (no skimping on product to save money). The rest of the section addresses the weighing of material. Two people must review each addition, unless that addition is done by an automatic process, than an one person check is sufficient. This rule also applies to calculations.

## Slide 22: 21 CFR 211 Part F Production and Process Controls 211.100-211.115
211.100 – Written procedures for the production to ensure the identity, strength, quality, and purity of the product. Creation of the product must documented (batch record) and any deviation from the process must be documented and justified.
211.101 – The creation of the product must be done to obtain 100% of the labeled amount of the active ingredient (no skimping on product to save money). The rest of the section addresses the weighing of material. Two people must review each addition, unless that addition is done by an automatic process, than an one person check is sufficient. This rule also applies to calculations.

## Slide 23: 21 CFR 211 Part F Production and Process Controls 211.100-211.115 -Continued
211.110- In process testing of each batch must occur to ensure the validity of the product. There must be specifications, which are derived from previous experience and should align with finish product testing. The testing needs to be reviewed by Quality control and rejected material must be quarantined to prevent use in the manufacturing process
211.111 – There should be time limits completion of each phase of manufacture to ensure quality. Deviations from the time limits must be documented and justified.

## Slide 24: 21 CFR 211 Part F Production and Process Controls 211.100-211.115 -Continued
211.113 – There must be written procedures, designed to prevent objectionable micro-organisms in drug products not required to be sterile. Written procedures are required and aseptic and sterilization processes must be validated.
211.115 – Reprocessing requires written procedures to take batches that do not confirm to process them into ones that confirm. The Quality Control unit must review and approve all reprocessing.

## Slide 25: 21 CFR 211 Part F Production and Process controls Application to Consultants and Related Computerized Systems
Consultants would be involved with the instrumentation that tests in process and finished product. If the batch record is electronic, that would need to be validated, along with any yield calculations and automated weight calculations.
There are many related systems for creation and testing of product.
Batch record systems that would keep track of all steps of the process include: Werum Pas-X.

## Slide 26: 21 CFR 211 Part G Packaging and Label Controls 211.122-211.137
211.122 – Written procedures for the identification, storage, handling, sampling, examination, and/or testing of labeling and packaging materials. The procedures must be followed.
  Labels must have specification and be tested for accuracy.
  Records for shipments of labels must be maintained. Any obsolete or expired labels must be destroyed.
  Labels for different drugs and strengths must be stored separate from each other. There are special requirements for “cut sheets” and “gang labels” (more than one type of label on a sheet)
  Labels must be inspected either by a person (100% verification) or by instrument.
  Printing of labels must be monitored to ensure accuracy.

## Slide 27: 21 CFR 211 Part G Packaging and Label Controls 211.122-211.137
211.125 – Control over the labels must be kept to ensure accuracy. Which labels used must be in the master batch record. The number of labels used must be reconciled and any extra labels either destroyed (if the label has the lot number) or stored properly for future use (no lot number on the label). Control procedures must be written

## Slide 28: 21 CFR 211 Part G Packaging and Label Controls 211.122-211.137
211.130 – Written procedures that the correct labels and packaging is used on drug product. Must prevent mix-ups and cross contamination. Blank containers cannot be mislabeled. Packaging needs to include a lot number. Inspection of labels and packaging to ensure accuracy must occur and go into the batch record. Any previous drugs should be cleared out before new product is labeled. All previous labels should be removed.
211.132 – The FDA has specific rules for tamper resistant packaging for OTC drugs.
211.134 – Finished drug products will be inspected to ensure the correct label and lot number. A representative sample will be visually inspected for correct labeling. The results of the inspection go into the batch or control record.

## Slide 29: 21 CFR 211 Part G Packaging and Label Controls 211.122-211.137
211.137 – The expiration date must be included on the drug product and be based on the stability testing. Expiration dates shall be related to storage conditions as based on stability testing. If the drug requires to be reconstituted, the expiration date of the original and reconstituted drug must be included. Homeopathic, Allergenic extracts and drugs under an IND are exempt from expiration dating

## Slide 30: 21 CFR 211 Part G Packaging and Labels Application to Consultants and Related Computerized Systems
Equipment used in the packaging and labeling process would be validated by Consultants along with the electronic master batch record software mentioned in the previous section.
Common electronic systems for verifying label content: Global Vision scanner.

## Slide 31: 21 CFR 211 Part H Holding and Distribution 211.142-211.150
211.142 – Written procedures for the warehousing of drugs are required. The procedures must include quarantine of product not released by QA. Temperature, humidity, and light are controlled so that the product is not affected.
211.150 - Written procedures for the distribution of drug products are required. The procedures must include rotation of stock so oldest product is used first (can be deviated from if appropriate). And a system to that tracks distribution of product in case a recall is required.

## Slide 32: 21 CFR 211 Part H Holding and Distribution Application to Consultants and Related Computerized Systems
Equipment used to track the product for recall purposes along with the environmental systems in the warehouse would be validated along with the electronic master batch record software mentioned in the previous section.
Common electronic systems for tracking distribution: SAP.

## Slide 33: 21 CFR 211 Part I Laboratory Controls 211.160-211.176
211.160 - All documents (specifications, standards, sampling plans, test procedures, or other laboratory control mechanisms) must be approved by QA.
Specifications related to drug products, closures, and containers etc. must include a description of the sampling and testing procedures used. Retesting of components susceptible to deterioration is required.
Conformance to written specifications and a description of sampling and testing procedures is required for in process materials. The samples must be representative and identified. This also applies to drug product (finished material)

## Slide 34: 21 CFR 211 Part I Laboratory Controls 211.160-211.176 – Continued
211.160 (cont) – Instruments and other devices used for testing must be used per SOPs, and calibrated. There must be a written program containing directions, schedules, limits for accuracy and precision for the instruments. Any instruments/devices that do not meet specifications must not be used.
211.165 – Each batch of product must be tested by the laboratory, which must include identity and strength. If necessary testing will occur to ensure there are no microorganisms.

## Slide 35: 21 CFR 211 Part I Laboratory Controls 211.160-211.176 – Continued
211.165 (cont) – Sampling and testing plan must be written which includes sampling method and number of samples. There must be acceptance criteria for all tests approved by QA. Test methods must be validated. Materials that don’t meet must requirements must be rejected.

## Slide 36: 21 CFR 211 Part I Laboratory Controls 211.160-211.176 – Continued
211.166 - There must be a written program for Stability Testing which will be used to determine appropriate storage conditions and expiration dates of product. The following items must be included in the program: sample size and test intervals, storage conditions, test methods, drug must be tested in same closure as it is sent, and reconstituted drugs must be tested prior and after reconstitution. Separate rules for homeopathic and allergen extract drugs.

## Slide 37: 21 CFR 211 Part I Laboratory Controls 211.160-211.176 – Continued
211.167 – Special Requirements, written procedures required for all of the following. For sterile and/or pyrogen-free drugs, special testing must occur to ensure the product meets the requirements. For ophthalmic ointment testing for abrasives/ harsh substances must be completed. For controlled release drugs (12 hour/24 hour drugs) testing must be completed to ensure rate of release

## Slide 38: 21 CFR 211 Part I Laboratory Controls 211.160-211.176 – Continued
211.170 – Reserve Samples Companies must keep a reserve samples from each batch of API and finished product. The amount must be at least 2x the amount needed to conduct all standard required tests for release. These must be kept 1 year after the expiration date for the batch.
There are separate rules for radioactive, OTC, sterile and pyrogen-free API and drug product.

## Slide 39: 21 CFR 211 Part I Laboratory Controls 211.160-211.176 – Continued
211.173 – Animals used in the testing of drug product (any stage) shall be controlled and maintained to ensure suitability of their intended use. They must be identified and there must be records of their use.
211.176 – If there is a non-penicillin drug that may have been contaminated by Penicillin. That drug must be tested per the standard listed in the regulations and not marketed if contaminated

## Slide 40: 21 CFR 211 Part I Laboratory Controls Application to Consultants and Related Computerized Systems
Software that runs each piece of laboratory equipment would be validated by Consultants.
Too many individual software to list, however, many companies are now using Empower to control all the HPLCs across all sites.
Software for all laboratory data to be stored for security and backup.
  This data can include, raw material, in process, finished product and stability testing data.
Common software used: Laboratory Information Management System (LIMS)

## Slide 41: 21CFR 211 Part J Records and Reports 211.180-211.198
211.180 – General: Any record created for the batch, laboratory, closures or containers will be kept 1 year after the expiration date (OTC has different rules). These records must be made available to the FDA and can be copied by the agency. Records may be original or kept as photocopy.
For each previous section where written procedures or records are required. This section details what would be in each record and retention requirements of the record by type.

## Slide 42: 21 CFR 211 Part J Records and Reports Application to Consultants and Related Computerized Systems
Validation is required of the systems that these records are kept in. These include previous systems referenced.
Laboratory systems will need to meets requirements set forth in 21 CFR 211.194
Common software used: Laboratory Information Management System (LIMS)
Complaint files are also covered in this section and would need to be validated.
Common software for complaints: TrackWise

## Slide 43: 21CFR 211 Part K Returned and Salvaged Product 211.204-211.208
Rules for Returned and salvaged product requirements are set forth in these sections.

## Slide 44: Relation to Good Clinical Practices and Good Laboratory Practices
The main areas that overlap is the requirement to validate laboratory instruments or larger data storage software (Documentum, LIMS, etc.)
From a regulatory point of view, many of the regulations don’t apply directly to consultants, but typically validate the systems that are incorporated to meet the regulations.

## Slide 45: Relation of GxPs to 21 CFR Part 11
21 CFR Part 11 regulations set forth the requirements for electronic records and electronic signatures.
When companies install electronic (computer) systems that were listed throughout this presentation to meet GxP requirements, they must be validated to meet Part 11 compliance.
The actual requirements for Part 11 are covered in a separate training.

## Slide 46
Questions?
This was a broad overview, and not inclusive.
COVEX, LLC