## Slide 1: Covex, LLC
Introduction to Risk

## Slide 2: What is Risk?
The potential adverse impact associated with the use of the specific product in the target environment. A description is provided of the risk to the business if the technology fails to operate or perform as expected.

## Slide 3: Intended Use & Risk
Just what is the system supposed to do?
How is it going to do it?
What are the anticipated risks? (Business, Technical, Safety, Regulatory)
How does this impact validation?

## Slide 4: Risk Assessments
A simple Risk Assessment process may be applied to automated systems to target validation efforts for those areas and functions that most require it.

## Slide 5: Risk Assessment – System Implementation
It is impractical to test every aspect of an automated system.
Therefore, Risk Assessment should be used to:
  Identify the critical areas/functions to test.
  Determine how rigorously to challenge each area/function of the system.
  Assess those risks associated with the operational phase of the automated system and not the ‘in-project’ risks.
  Allow the business to identify and minimize system malfunctions and deviations.
  Provide the necessary justification for the validation approach taken to support the system implementation.

## Slide 6: Risk Assessment – System Implementation
Benefits of Risk Assessment to System
Implementation:
  Defines system purpose and scope.
  Effective implementation of a system that meets the desired end user requirements.
  Verifies regulatory obligations and patient safety requirements are met.
  Allows for a cost effective system implementation.

## Slide 7: Evaluating Risk (System vs Requirement)
Risk at the System Level
  Systems that are of lower overall impact can be documented and tested less rigorously
  Risks that can not be eliminated by design should be reduced to an acceptable level by controls or manual procedures.
Risk at the Functional Requirement Level
  The results of functional risks assessments should influence the extent and rigor of verification.
  Rigorous testing can be applied to the testing and control of functions that are of the highest risk with less rigor applied to low risk functionality.

## Slide 8: Risk can be managed by:
Elimination by design (COTS vs Custom Code)
Reduction to an acceptable level
Verification to demonstrate that risks are managed to an acceptable level.

## Slide 9: Identifying Risk in the SDLC/SVLC Process:
Risk Assessments should be conducted at several stages of a project.
The number and timing of the assessments should be documented in the Validation Plan.

## Slide 10: Identifying Risk in the SDLC/SVLC Process:
Vendor Audits
  A risk decision point on whether or not re-test vendor verified capabilities common to all clients OR whether or not to buy the system or engage a specific vendor
  Most vendors are selected or engaged prior to this occurring
Project Kickoff
  To define the validation process/deliverables
Requirement Level
  Development of the User Requirement Specification (URS) and Functional Specification (FS).
  To define testing approach for specific capabilities.
The completion of the Design Review prior to validation test.
Whenever any major changes are to be applied to the system.

## Slide 11: Identifying Risk in the SDLC/SVLC Process:

## Slide 12: Risk generally has 3 components:
Probability of occurrence
Likelihood of detection
Severity of undesired effects

## Slide 13: Probability of Occurrence
What is the likelihood of a problem occurring?
Consider the type / complexity of the system
Consider the technology of the system (bleeding edge or trailing edge)
Set a scientifically justifiable standard
Off The Shelf (OTS) vs Custom Code

## Slide 14: Probability of Occurrence – Classification
Example
Low: The event may occur once per ten thousand transactions or more
Medium: The event may occur once per thousand transactions
High: The event may occur once per hundred transactions

## Slide 15: Probability of Detection
Harder with Hardware than Software
Software Testing alone cannot guarantee risks have been identified / mitigated
Contributes to the overall risk level
Set a scientifically justifiable standard

## Slide 16: Probability of Detection - Classification
Example
Low: Detection of the problem is unlikely (e.g. less than 1 event in every 3 transactions or operations)
Medium: Detection of the problem reasonably likely (e.g. 1 event in every 2 transactions or operations)
High: Detection of the problem is highly likely (e.g. 1 event in every 1 transactions or operations)

## Slide 17: Severity of the Undesired Effect
If something does go wrong – how bad will it be?
Set a scientifically justifiable standard

## Slide 18: Severity of the Undesired Effect
Classification Example
Low: A minor negative impact with short term effects.
Medium: A moderate impact that could have short- to medium-term detrimental effects.
High: A significant negative impact with long-term effects and potentially catastrophic short-term effects.

## Slide 19: Just what is the system supposed to do?
Start with the top level Business/User Requirements
Maybe a statement of need or purpose
“We need a three way tree swing”
Should be done for all systems (validated or not)

## Slide 20: So What are some Risks?
Business
Corporate reputation
Economic impact
Inability to perform key business functions

## Slide 21: So What are some Risks?
Technical
  Equipment downtime
  Equipment damage
  Damage to other systems
  Lost/Corrupted Data

## Slide 22: So What are some Risks?
Regulatory
  Incorrect/ lost / corrupted data for the support of regulatory submissions
  Inability to retain / lost records still under their retention period
  Loss of product traceability
  Inability to support regulatory inspections

## Slide 23: So What are some Risks?
Safety
  Incorrect batch process
  Raw material errors
  Integrity of laboratory results
  Safety of patients / caregivers
  Labelling errors

## Slide 24: So you made a list of risks…
You determined how likely each one was to occur
You determined how likely each one was to be detected
You determined how severe each one would be if it occurred
Now what?

## Slide 25: How significant are they?
High Risk (H): Direct negative impact on pharmaceutical quality, patient safety, and/or data integrity
Medium Risk (M): Indirect regulatory and/or data integrity impact (e.g., SOP or training records management)
Low Risk (L): No GxP impact

## Slide 26: Weight Detection Probability
High Risk (H): Difficult to detect during normal use
Medium Risk (M): May not be detected during normal use
Low Risk (L): Highly likely to be detected

## Slide 27: Weight Likelihood
High Risk (H): Very likely to occur
Medium Risk (M): May occur
Low Risk (L): Not likely to occur

## Slide 28: Other methods
You assign a weight or numeric value to each
For example
  High = 3
  Medium = 2
  Low =1
Then add or multiply values
This can skew results

## Slide 29: GAMP method
First identify all the potential failure points
Second determine severity if a failure were to occur
Third, assign a value to severity (such as Low, Medium, High)

## Slide 30: GAMP method
Then determine how likely each failure is to occur
Give it the same rating (L, M, H)
Then assess the probability of detection if a failure were to occur
Assign it a rating as well (L, M, H)
Finally, come up with an overall risk level

## Slide 31: Examples…

## Slide 32: Examples (Part 2)…

## Slide 33: Issues with Identifying Risk
Companies use elaborate risk assessments for system and requirement levels, but never use the evaluation as intended.
More conservative companies will test everything to the fullest no matter the evaluation while other companies will do next to no testing.

## Slide 34: Issues with Identifying Risk
Risk Classification: High
  Predicate rules apply
  Safety and efficacy of the product
  Damage to manufacturing, packaging and lab equipment
  High cost of production interruptions
  Impact on quality of product

## Slide 35: Issues with Identifying Risk
Risk Classification: Medium
  Medium frequency of production interruptions
  High frequency of failure or breakdown of equipment without damage to the product
Risk Classification: Low
  No impact on quality of product
  Low frequency of failure or breakdown of equipment without damage to the product
  Low frequency of production interruptions

## Slide 36: Predicate Rules & Risk
What is the intended use of the system?
Will a document management system have the same risk as an Adverse Event recording system?
What is the nature of the record (is it one that needs to be retained forever?)

## Slide 37: Predicate Rules & Risk
Is the system likely to contain records that could entice someone to falsify?
Are there records that require regulatory submission?
Have the requirements determined the official record?
Do the records cover more than one GxP area?

## Slide 38: Predicate Rules & Requirements
Do your requirements ensure compliance with predicate rules (esp the record retention ones!)
Do your predicate rules require general signings?
Consider the intertwining of predicate rules and Part 11 in your requirements

## Slide 39: Risk – Key Points to remember
Start identifying risks as soon as the intended use is known
Assess the risks using sound logical/scientific/justifiable means
Document the risks
Identify appropriate mitigations
Ensure the risks are mitigated

## Slide 40
Questions?
COVEX, LLC